## Slide 1: High Density Neural Implant Cylindrical Packaging
Neuralink, US 2023/0063165 A1, Published 3/2/2023
6/15/2024

## Slide 2: Background
Space of Neural Implants:
Large implants – prone to tissue damage
Constant pressure to reduce overall volume
Most electronic components – stacked on top of one another
Need compact, dense packaging
Accessibility of Neural Implants:
Power source - often charged wirelessly (via induction coil) to reduce infection risk
Data transmission - rely on radio transmission
High-performance, specialized chips needed for collecting/processing neural signals

## Slide 3: Outline
Goal: Describe space-saving configuration of BCI with >= 4 circuit boards forming sides of >= 5-sided geometric prism
Embodiments:
  Side-Top view of Assembly of Cylindrically Wrapped Electronics with Chassis
  Arrangements of Circuit Boards to form various Geometric Prisms
  Side-Top view of Assembly of Cylindrical Power Coil
  Side-Top view of Assembly of Cylindrically Wrapped Electronics and Circular Circuit Board
  Side-Top view of Assembly of Cylindrically Wrapped Electronics with Chassis, Circular Circuit Board, and Battery
  Side-Top view of Ferrimagnetic Cup and Cylindrical Power Coil Assembly
  Side-Top view of Ferrimagnetic Cup, Circular Loop Antenna, and Cylindrical Power Coil Assembly
  Bottom view of Ferrimagnetic Cup and Circular Circuit Board Assembly including Alignment Features
  Side-Bottom Cutaway view of Assembly of Ferrimagnetic Cup + Cylindrically Wrapped Electronics including Alignment Features
  Vertical Cross-Section of High-Density Neural Implant

## Slide 4: Side-Top view of Assembly of Cylindrically Wrapped Electronics with Chassis
7 Circuit boards (PCBs)
(Arranged cylindrically to form a polygon base prism sides)
Chassis
(restrain each component to form prism)
Power connectors
(connect to button-cell battery)
Antenna connector
(couples circuit boards with radio antenna)
Notch
(align chassis with other components)
Support structures
Electrical components
(e.g., resistors, transistors, inductors, etc.)
Circular base
Flex cables
(connect circuit boards)
Power coil connector
(wireless charging coil – charge battery)

## Slide 5: Arrangements of Circuit Boards to Form Various Geometric Prisms
Boards – wrapped at least halfway
Circuit board
Polygon base
At least 4 circuit boards

## Slide 6: Side-Top view of Assembly of Cylindrical Power Coil
Power coil
Aluminum, copper, silver, gold, etc.
Conduct power to electrical components
Height
1st End
2nd End
Layers
Cylindrical-wrapped coil:
Reduces overall height
Less loss at lower total volume (higher surface-area vs volume ratio)

## Slide 7: Side-Top view of Assembly of Cylindrically Wrapped Electronics and Circular Circuit Board
Circular circuit board
(any PCB)
IC chips
(e.g., ASIC, FPGA, etc.)
Connector
(distribute power from circular circuit board to individual circuit boards)
Notch
(for alignment)
Flex cables
Circuit board
Power connector
Power coil connector
Antenna connector

## Slide 8: Side-Top view of Assembly of Cylindrically Wrapped Electronics with Chassis, Circular Circuit Board, and Battery
Cylindrical button battery
Provide power to 1+ optical components disposed on a plurality of circuit boards
Includes cathode casing + anode cap
Chassis
Flex cables
Circular circuit board
Circuit board
Power connector
Power coil connector

## Slide 9: Side-Top view of Ferrimagnetic Cup and Cylindrical Power Coil Assembly
Ferrimagnetic cup
Made of sintered ferrite
Shields components within cup from external electromagnetic interference (EMI) via power coil
Shields EMI from interfering with functionality of radio antenna/leaking into neural pathways of patient
Radio antenna
Circular loop – reduce overall height
Large diameter – better average gain, more uniform beam pattern
Antenna connector

## Slide 10: Side-Top view of Ferrimagnetic Cup, Circular Loop Antenna, and Cylindrical Power Coil Assembly
Ferrimagnetic cup
(separates power coil from any circuit board(s) – reduce EMI from external coupling)
Radio antenna
Power coil
Antenna connector

## Slide 11: Bottom view of Ferrimagnetic Cup and Circular Circuit Board Assembly including Alignment Features
Bump
Notch
Circular circuit board
Antenna connector
Power coil connector
Ferrimagnetic cup

## Slide 12: Side-Bottom Cutaway view of Assembly of Ferrimagnetic Cup + Cylindrically Wrapped Electronics including Alignment Features
Ferrimagnetic cup
Power coil connector
Cylindrical button battery
Chassis
Power connector
Antenna connector
Notch
Connector
Circuit board
Bump
(mate w/ opening of connector)

## Slide 13: Vertical Cross-Section of High-Density Neural Implant
Power coil connector
Circuit board
Antenna connector
Chassis
Connector
Power coil
Cylindrical button battery
Housing
Any body-save material
Cylindrical
Height – maximize efficiency while reducing tissue erosion
Electrical leads
Passes thru opening of housing, into neural tissue
Transmit electrical impulses between surrounding tissue and components of neural implant
Radio antenna
Ferrimagnetic cup
Metallic shield
Reduce EMI effects on electronic components
Reduce unwanted humidity accumulation
Circular circuit board
Dielectric substrate
Conductor

## Slide 14: Flowchart for Manufacture

## Slide 15: Step 1:

## Slide 16: Step 2:

## Slide 17: Step 3:
Flex cable

## Slide 18: Step 4:
Chassis

## Slide 19: Step 5:
Power coil

## Slide 20: Step 6:
Ferrimagnetic cup

## Slide 21: Step 7:
Radio antenna
Antenna connector

## Slide 22: Step 8:
Circular circuit board

## Slide 23: Step 9:
Metallic shield