## Slide 1: Optical Coherence Tomography for Robotic Brain Surgery
Neuralink, US 2021/0007808 A1, Published 1/14/2021
6/26/2024

## Slide 2: Background
Brain implants require delicate control for secure insert & attachment
Computer vision for surgical robotic surgery becomes problematic in discerning varying layers in brain + shadows casted via surgical tools, already implanted electrodes, etc.
Implantation with specific accuracy becomes difficult in the presence of background movement (e.g., blood flow, natural brain movement, breathing, heart rate), fluid membrane on brain surface, and determining proper depth for implantation

## Slide 3: Outline
Goal: Describe application for guiding robotic surgical systems via optical coherence tomography (OCT) by acquiring depth maps of wet brain surface or other tissue surfaces
Embodiments:
  System Overview
    Robotic Surgery System using Optical Coherence Tomography (OCT)
    Close-up bottom view of system
    Overhead Image of a Portion of Brain
    3D Image showing Surface Topology of Brain
    Cross-Section of Head with Portion of Skull Removed
  Real-Time Imaging Process: Optical Coherence Tomography (OCT)
  Electrode Implantation – Why OCT Alone is Not Sufficient
    Implantation of Electrodes in Target Tissue Proxy Substance
    Electrodes implanted in brain tissue
    Shadows Cast By Threads
    Occlusions Casted from Fluid & Vessels
  Example Computing System + Components

## Slide 4: Robotic Surgery System using Optical Coherence Tomography (OCT)
Inserter Head
Device engagement subsystem
Ultrasonic Cleaner

## Slide 5: Close-up bottom view of system
OCT sensor

## Slide 6: Overhead Image of a Portion of Brain
Vasculature
(need to be avoided during surgery!)
Avoid vasculature during brain surgery
Can select needle insertion location automatically

## Slide 7: 3D Image showing Surface Topology of Brain
Brain surface undulating (dynamic)
Blood vessel
(pulsating)
Subarachnoid space
The environment is complex, dynamic – surgery must adapt for factors that impact precision + accuracy!
Very challenging to process & understand brain surface quickly to guide inserter head

## Slide 8: Cross-Section of Head with a Portion of Skull Removed

## Slide 9: Optical Coherence Tomography (OCT)
Used to guide a robotic system to surgically implant electrodes
Can quickly generate depth maps of brain surfaces to ensure precision of surgical robotic system
Performed by OCT sensor
  Obtain stack of 2D arrays of intensity values (light bouncing back to sensor)
  Can obtain tens of millions of points
  Each slice – different depth layer
  120-160 slices in a stack
  May select 10-30 slices based on spatial selection for targeted insertion sites

## Slide 10: Flowchart for Guiding Robotic Surgery via Optical Coherence Tomography

## Slide 11: Step 1:
Example Slice
- Stack of slices captured by OCT sensor
- OCT sensor – top of figure, facing downward
- Each slice imaged at a particular depth
Problem: OCT may pick up background signal/noise artifacts

## Slide 12: Step 2:
Spatial Smoothing:
Smooths out intensity values to filter out low signal + noise artifacts
e.g., Gaussian blur, median blur, bilateral blur, etc.
Fig. 6 uses Gaussian blur

## Slide 13: Step 3:
Performed by processing unit
K-means method:
White spots – above threshold value
Dark spots – below threshold value
Threshold – based on known pixel intensities for measured brain surface
Alternatively: Can also use Otsu’s method to minimize (or maximize) intraclass variance

## Slide 14: Step 4:
Connected component analysis:
- Identify “blobs” (regions of threshold intensity values forming continuous structures)
- Look for continuity in each segmented slice
- Evaluate whether region fulfills qualifying pixel size

## Slide 15: Step 5:
Filtered out!
(below 50% of slide width)
Keep this blob
(above 50% of slide width)
Size of blobs – can use continuity length as threshold

## Slide 16: Step 6:
Identify an edge on blob that is not filtered in step 5
Resultant edge of top edge blob 801

## Slide 17: Step 6.5: Apply Image Derivatives to Compile 32-bit Depth Map
Portion of skull
Brain surface
(can be seen along bottom of depth map to guide robot inserter head)
Problem:
Noise produced via image derivatives - does not account for shadows of other electrodes in brain (detected surface much higher than actual)

## Slide 18: Step 7:
Brain surface
Portion of skull
Solution: Selective median filter
Identify median points along edges
Filters out noise + artifacts
Forms 3D surface topography
Selective mean filter – selects only a location in space (instead of valid surface location)

## Slide 19: Step 8:
Brain surface
Portion of skull

## Slide 20: Overall Procedure Flow Map
Series of Slices
Example Slice
Blurred Slice
Segmented Slice
Blobs Detected
Edge Detection Slice
Depth Map
3D Render
Spatial smoothing
Thresholding
Filter
(based on sizes)
Edge Detection
Selective Median Filter
Guide Robotic End Effector
Image Derivatives
Connected Component analysis
Blobs Filtered Out

## Slide 21: Implantation of Electrodes in Target Tissue Proxy Substance
Target tissue proxy substance
Inserter head
Needle
2nd Thread
1st Thread
2nd Thread
1st Thread
1. Pre-implantation
2. Lowering of Surgical Robotic End Effector
3. Insertion of electrode
4. Final electrode left

## Slide 22: Electrodes implanted in brain tissue
Threads in close proximity
96 threads
32 electrodes per thread (total 3,072 electrodes)
Thread:
width 5-50µm
thickness 4-6µm
length 20mm
Several initially inserting threads can cast shadows – impact later threads

## Slide 23: Shadows Cast By Threads
Brain surface
Thread that casts a shadow
Drop in intensity due to above thread 1402
Thread(s) that cast shadows results in inaccurate portrayal of region
Brain surface
Drop in intensity
Threads that cast shadows
Artifacts
Single Thread
Multiple Threads

## Slide 24: Occlusions Casted from Fluid & Vessels
Vessels, Vasculatures, etc.
Brain surface
High intensity regions
Arachnoid space
CSF flowing along brain (OCT sensor has trouble picking up)
Shadows
(cast from fluid and vessels along surface of brain)
High intensity regions
High intensity regions
Shadows cast from fluid and vessels
OCT data alone (without processing) is less precise
Selective median filter removes noise/artifacts

## Slide 25: Example Computing System

## Slide 26: Components for Example Computing System