## Slide 1: Automatic Craniotomy and Bonework via Milling, Force Sensing, and Impedance Sensing
Neuralink, US 2023/0165594, 6/1/2023
4/18/2024

## Slide 2: About Craniotomy
Craniotomy – neurosurgical procedure of creating surgical perforation of cranium to access intracranial structures (brain)
Very time-consuming & high risk – requires manual cutting or drilling by a physician
Safety risks – requires perforation to be close to intracranial structures, causing damage to the intracranial structures
Accuracy – craniotomy not deep enough means insufficient access for signal
Consistency – irregular drilling surface may cause dimensions & angle of perforation relative to cranium
Very costly to hire physicians highly skilled physicians

## Slide 3: Outline
Goal: Introduce an automatic craniotomy milling system using a computer numerical control (CNC) machine , via instructions from a controller based on input values from sensors detecting axial force of working tip and bio-impedance of patient
Embodiments:
  Front perspective view of end effector of CNC machine
  Rear perspective view of end effector of CNC machine
  Bio-impedance measurement at various depths within cranium
  System architecture of craniotomy milling system
  2D view of a milling operation
  3D view of a milling operation
  Flowchart of performing a craniotomy
  Flowchart of plunge milling a plurality of holes in cranium
  Another flowchart of performing a craniotomy

## Slide 4: Front perspective view of end effector of CNC machine

## Slide 5: Rear perspective view of end effector of CNC machine

## Slide 6: Bio-impedance measurement at various depths within cranium
High impedance – more force to drill (more “solid bone”)
Low impedance – less force to drill (more “fluid”)
Outer layers have higher impedance
Bio-impedance system – circuitry system
  Power (A/C Voltage) source in mono-polar config
  May include supply contact (anode) that couples to end mill
  Supply contact in commutator brush
NOTE: Can measure raw impedance (with various components like commutator brush, end mill, return contact) or adjusted/scaled impedance

## Slide 7: System architecture of craniotomy milling system

## Slide 8: System architecture of craniotomy milling system
Key idea: STOP milling when you break through inner layer of cortical bone and reach the dura
How to tell CNC to “stop milling”?
 change milling parameters
How can we accurately tell when to “stop milling”?
Multi-fault tolerance:
Can have multiple conditions from different input data - ANY condition satisfied warrants a stop
Check & compare multiple input data in processor for better consistency

## Slide 9: System architecture of craniotomy milling system – axial force implementation 1
Input recent axial force sensor data (a) to processor via cable
Pass a to memory
Memory stores:
  Historical axial force data (a_h) from other patients
  A range [a_min, a_max] from current operation
Processor appends a to current axial force data
Compare a with a_h OR a from previous iteration  Determine depth d of end mill
Stop CNC milling (adjust milling params) when desired depth d is reached

## Slide 10: System architecture of craniotomy milling system – axial force implementation 2
Input recent axial force sensor data (a) to processor via cable
Pass a to memory
Memory stores:
  Historical axial force data (a_h) from other patients
  A range [a_min, a_max] from current operation
Processor calculates range of axial force data [a_min, a_max] in current milling action
Stop CNC milling (adjust milling params) when a < 80-90% of a_max OR when a < a_min

## Slide 11: System architecture of craniotomy milling system – bio-impedance implementation
Input recent bio-impedance sensor data (i) from bio-impedance measuring system to processor
Pass i to memory
Memory stores
  Historical impedance data (i_h) from other patients
  Current impedance data (i) for current operation
Processor appends i to current impedance data
Compare i with i_h OR i from previous iteration  Determine depth d of end mill
Stop CNC milling (adjust milling params) when desired depth d is reached
Bio-impedance sensor data – between return contact and supply contact on end effector

## Slide 12: System architecture of craniotomy milling system – Overall implementation
Scan data - performed as a scan BEFORE craniotomy on the patient (patient-specific)
  e.g., CT scan, ultrasound, etc.
User input data - from physician / doctor, inputted before OR during craniotomy
  e.g., milling params, historical axial force / bio-impedance from previous procedures, CNC machine params like end mill type & size

## Slide 13: System architecture of craniotomy milling system – Overall implementation
Input patient’s scan data, user input data into memory
Input axial force sensor data (a) & bio-impedance sensor data (i) into processor
Memory stores:
  Historical axial force data (a_h) from other patients
  A range [a_min, a_max] from current operation
  Historical impedance data (i_h) from other patients
  Current impedance data (i) for current operation
If ANY of these conditions are satisfied:
  Axial force out of specified range of current milling
  LARGE change of axial force
  Axial force has reached desired depth
  Bio-impedance has reached desired depth
  Bio-impedance very different from historical data
  LARGE change of bio-impedance
STOP the milling

## Slide 14: 2D view of a milling operation
Need multiple milling tasks to ensure better precision & accuracy (allowing varying depths at various locations)
# of boreholes, # of milling operations, radius from craniotomy center – preselected via user input data
Face mill path shape can also be oval, rectangular, etc.

## Slide 15: 3D view of a milling operation
Boreholes form borehole paths with borehole final depths
Borehole final depths – determined by processor based on input data

## Slide 16: Flowchart of performing a craniotomy

## Slide 17: Step 1:
Drill locations
Craniotomy center
X

## Slide 18: Step 2:
Holes
X

## Slide 19: Step 3:
X
Face mill path

## Slide 20: Flowchart of plunge milling a plurality of holes in cranium

## Slide 21: Step 1:

## Slide 22: Step 2:
Bio-impedance

## Slide 23: Step 3:
Axial force sensor
Controller

## Slide 24: Step 4:
Controller
Impedance OR axial force change stop condition reached?
 STOP!!

## Slide 25: Step 5:
Final depth recorded in memory

## Slide 26: Another flowchart of performing a craniotomy

## Slide 27: Step 1:
Electrical contact

## Slide 28: Step 2:
Outer surface of cranium

## Slide 29: Step 3:

## Slide 30: Step 4:
Bio-impedance

## Slide 31: Step 5:
Controller
Axial force sensor

## Slide 32: Step 6:
Controller
Axial force sensor
Impedance OR axial force change stop condition reached?
 STOP!!