## Slide 1: Cannula for Grasping and Setting Lead with Needle
Neuralink, US 2023/0310028 A1, Published 10/5/2023
6/19/2024

## Slide 2: Background
Brain-machine interfaces (BMIs) require fine-scale communication (at the neuron level)
Advanced BMIs require increasing # of neurons by many orders of magnitude  multiple lead-bearing electrodes
Implanting electrodes requires extreme precision – micron/sub-micron scale
Each lead should be held in place for accurate implantation
Equipment for guiding leads must be cleanly detached from needle after implantation

## Slide 3: Outline
Goal: Describe a system for a lead, needle, and cannula sized and shaped for ease of needle threading and positioning (e.g., implantation into biological tissue)
Embodiments:
  About the System
    Cannula, Needle, and Lead in 1st + 2nd Configurations
    Cannula, Needle, and Lead
    Cannula Photographs
    Close-Up Views of Cannula
    Lead with Expanded Region
    Needle with Ledge
    Close-Up Views of Lead and Needle
    Example Geometry of Lead and Needle
  Engagement + Implantation Techniques:
    Needle, Lead and Cannula
    Lead Engaged with Needle and Cannula
    Multiple Leads Disposed for Implantation
    Apparatus for Implantation and Engagement of Lead
    Close-Up View of Apparatus for Implantation and Engagement of Lead
    Flowchart for Engagement & Implantation of Lead
    Computer System

## Slide 4: Cannula, Needle, and Lead in 1st Configuration
Cannula
Needle
Lead
Biocompatible (e.g., polyimide)
Include conductive material (e.g., thin gold trace) deposited in polyimide substrate to transmit information
Up to 3 layers of insulation, 2 layers of conductor
Include many wires with small electrodes
Lead
Needle
Cannula
Side View
Front View
Exit Gate
Ledge
Indentation
(allows opening to prevent needle from colliding to back wall of cannula)
2nd Side
Expanded Region
Opening
Slot
Aperture
1st Side
1st Side
1st Config: Needle and lead held in place via respective geometry

## Slide 5: Cannula, Needle, and Lead in 2nd Configuration
2nd Config: Needle and lead positioned lower wrt cannula
Cannula
Needle
Lead
Needle
Cannula
Lead
Side View
Front View

## Slide 6: Cannula, Needle, and Lead
Front View
Side View
Cross-sectional View
Cannula
Scale
Needle
Exit gate
Ledge
Cylindrical cavity
Needle
Cannula
Exit gate
(holds lead in place via its geometry)

## Slide 7: Photographs of Cannula
Side View
Front View
Indentation
Exit gate
Slot
Aperture

## Slide 8: Close-Up Views of Cannula
Side View
Front View
Indentation
(facilitate cleaning, improve visibility of cameras)
Top of Indentation
Top of Aperture
Aperture
Aperture height
(2/3 of aperture width, ~0.04m)
Aperture width
(~0.069m)
Slot
Slot width
(2x slot height, 0.022m)
Slot height
(1/4 aperture height, 0.011m)
Higher than top of aperture – mitigate risk of lead clipping on the rear wall of the cannula

## Slide 9: Lead with Expanded Region
Expanded region height
(~5-6x needle width, ~3-4x opening height)
Expanded region width
(~1.5-5x 2nd region width, ~1.1-1.5x needle width, to prevent premature exit of cannula during seating of lead)
Expanded region
2nd region
Opening
2nd region width

## Slide 10: Needle with Ledge
1st portion
2nd portion
Ledge

## Slide 11: Close-Up View of Lead and Needle
Ledge
Lead
Needle
Opening
Tip of needle
Opening
ID_h-loop
ID_h-ir
Margin

## Slide 12: Close-Up View of Lead and Needle

## Slide 13: Example Geometry of Lead and Needle

## Slide 14: Close-Up View of Lead and Needle
Leftover radius height
Seating angle

## Slide 15: Needle, Lead and Cannula
Before Engagement
Towards Engagement Position
During Engagement with Lead
Towards Engagement Position
Temporary attachment surface
Cannula
Opening
Needle
Lead
Needle
Lead
Exit gate aperture
Cannula
Ledge
Tip

## Slide 16: Lead Engaged with Needle and Cannula
Lead
Needle
Cannula
Circuitry assembly
Include storage package structure with circuitry
Remains in-vivo of subject
Temporary attachment surface
(flexible backing made of silicon or parylene)
Antenna
Brain
2nd end of lead
(left implanted in brain)
Cranium
1st end of lead
(disposed in circuitry assembly)
2. Peel lead off temporary attachment surface
3. Drive lead to implantation side
1. Dispose lead on a temporary attachment surface

## Slide 17: Multiple Leads Disposed for Implantation
Circuitry assembly
Temporary attachment surface
Multiple leads
Needle
Cartridge

## Slide 18: Apparatus for Implantation and Engagement of Lead
Cartridge
Robotic arm
Cameras
Needle
Microprocessor controller
Cameras
Cameras
Robotic arm
Cartridge
Needle

## Slide 19: Close-Up View of Apparatus for Implantation and Engagement of Lead
Needle
Cartridge
Robotic arm
Drape / cloth
(sterile, replaceable)
Kinematic coupler
(redirect imaging path from cameras, sterile mounting for needle + cartridge)
Motor
Cartridge
Needle

## Slide 20: Flowchart for Engagement & Implantation of Lead

## Slide 21: Step 1:

## Slide 22: Step 2:

## Slide 23: Step 3:

## Slide 24: Step 4:

## Slide 25: Step 5:

## Slide 26: Step 6:
Brain

## Slide 27: Step 7:
Brain

## Slide 28: Step 8:
Brain

## Slide 29: Computer System